**************************Default**************************

catzip-icestorm
Risc-V servant
initial build
service
09/08/21

**************************Default**************************

devel@mypi3-20:~/WORKSPACE $ export WORKSPACE=/home/devel/WORKSPACE/
devel@mypi3-20:~/WORKSPACE $ export SERV=/home/devel/WORKSPACE/fusesoc_libraries/serv
devel@mypi3-20:~/WORKSPACE $ fusesoc run --target=verilator_tb servant --vcd --uart_baudrate=57600 --firmware=$SERV/sw/zephyr_hello.hex
INFO: Preparing ::serv:1.1.0
INFO: Preparing ::servant:1.1.0
INFO: Setting up project

INFO: Building simulation model
verilator -f servant_1.1.0.vc --trace
make -f Vservant_sim.mk
make[1]: Entering directory '/home/devel/WORKSPACE/build/servant_1.1.0/verilator_tb-verilator'
g++ -I. -MMD -I/usr/local/share/verilator/include -I/usr/local/share/verilator/include/vltstd -DVM_COVERAGE=0 -DVM_SC=0 -DVM_TRACE=1 -faligned-new -fcf-protection=none -Wno-bool-operation -Wno-sign-compare -Wno-uninitialized -Wno-unused-but-set-variable -Wno-unused-parameter -Wno-unused-variable -Wno-shadow -std=gnu++14 -Os -c -o servant_tb.o ../src/servant_1.1.0/bench/servant_tb.cpp
g++ -I. -MMD -I/usr/local/share/verilator/include -I/usr/local/share/verilator/include/vltstd -DVM_COVERAGE=0 -DVM_SC=0 -DVM_TRACE=1 -faligned-new -fcf-protection=none -Wno-bool-operation -Wno-sign-compare -Wno-uninitialized -Wno-unused-but-set-variable -Wno-unused-parameter -Wno-unused-variable -Wno-shadow -std=gnu++14 -Os -c -o verilated.o /usr/local/share/verilator/include/verilated.cpp
g++ -I. -MMD -I/usr/local/share/verilator/include -I/usr/local/share/verilator/include/vltstd -DVM_COVERAGE=0 -DVM_SC=0 -DVM_TRACE=1 -faligned-new -fcf-protection=none -Wno-bool-operation -Wno-sign-compare -Wno-uninitialized -Wno-unused-but-set-variable -Wno-unused-parameter -Wno-unused-variable -Wno-shadow -std=gnu++14 -Os -c -o verilated_dpi.o /usr/local/share/verilator/include/verilated_dpi.cpp
g++ -I. -MMD -I/usr/local/share/verilator/include -I/usr/local/share/verilator/include/vltstd -DVM_COVERAGE=0 -DVM_SC=0 -DVM_TRACE=1 -faligned-new -fcf-protection=none -Wno-bool-operation -Wno-sign-compare -Wno-uninitialized -Wno-unused-but-set-variable -Wno-unused-parameter -Wno-unused-variable -Wno-shadow -std=gnu++14 -Os -c -o verilated_vcd_c.o /usr/local/share/verilator/include/verilated_vcd_c.cpp
/usr/bin/perl /usr/local/share/verilator/bin/verilator_includer -DVL_INCLUDE_OPT=include Vservant_sim.cpp Vservant_sim_servant_sim.cpp Vservant_sim_servant__Mz1_MB2000_S1.cpp Vservant_sim_servant_ram__pi1.cpp Vservant_sim__Dpi.cpp Vservant_sim__Trace.cpp Vservant_sim__Slow.cpp Vservant_sim_servant_sim__Slow.cpp Vservant_sim_servant__Mz1_MB2000_S1__Slow.cpp Vservant_sim_servant_ram__pi1__Slow.cpp Vservant_sim__Syms.cpp Vservant_sim__Trace__Slow.cpp > Vservant_sim__ALL.cpp
g++ -I. -MMD -I/usr/local/share/verilator/include -I/usr/local/share/verilator/include/vltstd -DVM_COVERAGE=0 -DVM_SC=0 -DVM_TRACE=1 -faligned-new -fcf-protection=none -Wno-bool-operation -Wno-sign-compare -Wno-uninitialized -Wno-unused-but-set-variable -Wno-unused-parameter -Wno-unused-variable -Wno-shadow -std=gnu++14 -Os -c -o Vservant_sim__ALL.o Vservant_sim__ALL.cpp
Archive ar -cr Vservant_sim__ALL.a Vservant_sim__ALL.o
g++ servant_tb.o verilated.o verilated_dpi.o verilated_vcd_c.o Vservant_sim__ALL.a -o Vservant_sim
make[1]: Leaving directory '/home/devel/WORKSPACE/build/servant_1.1.0/verilator_tb-verilator'
INFO: Running
INFO: Running simulation
Loading RAM from /home/devel/WORKSPACE/fusesoc_libraries/serv/sw/zephyr_hello.hex
***** Booting Zephyr OS zephyr-v1.14.1-4-gc7c2d62513fe *****
Hello World! Service

The image below is suppose to look like the first seven lines when the sudo config_cat ~/servant_1.1.0.bin. The first seven lines are when iCE40 FPGA is programmed with
sudo config_cat helloworld.bin in the testbuilds/catzip/rtl/uart folder.

A pmodusb is connected to PM2 on Catboard.

CatBoard

Raspberry Pi 3B+ is running Raspberry Pi OS.

The USB is connected to The USB on Raspberry Pi3B+ which also has a catboard mounted on the 40 GPIO connector.

The serial port is setup as follows.

Other tools required are icestorm, yosys, nextpnr, and verilator.

Needed to install fusesoc

pip3 install --upgrade --user fusesoc

fusesoc --version
1.12.0

Forked https://github.com/olofk/serv

git clone git@github.com:develone/serv.git

Created a Pull request.

mkdir WORKSPACE

cd WORKSPACE/

export WORKSPACE=/home/devel/WORKSPACE/

echo $WORKSPACE
/home/devel/WORKSPACE/

export SERV=/home/devel/WORKSPACE/fusesoc_libraries/serv

echo $SERV
/home/devel/WORKSPACE/fusesoc_libraries/serv

fusesoc library add fusesoc_cores https://github.com/fusesoc/fusesoc-cores

fusesoc library add serv https://github.com/olofk/serv

cp ~/serv/servant.core ~/WORKSPACE/fusesoc_libraries/serv/
cp ~/serv/data/catzip.pcf ~/WORKSPACE/fusesoc_libraries/serv/data

fusesoc run --target=catzip servant creates the folder
build/servant_1.1.0/catzip-icestorm/
blinky.hex servant_1.1.0.bin servant_1.1.0.mk
edalize_yosys_procs.tcl servant_1.1.0.blif servant_1.1.0_next.asc
edalize_yosys_template.tcl servant_1.1.0.eda.yml yosys.log
Makefile servant_1.1.0.edif zephyr_hello.hex
next.log servant_1.1.0.json

serv/servant/service.v

`default_nettype none
module service
(
 input wire i_clk,
 output wire q);

   parameter memfile = "zephyr_hello.hex";
   parameter memsize = 8192;
   parameter PLL = "NONE";

   wire wb_clk;
   wire wb_rst;

   servant_clock_gen #(.PLL (PLL))
   clock_gen
     (.i_clk (i_clk),
      .o_clk (wb_clk),
      .o_rst (wb_rst));

   servant
     #(.memfile (memfile),
       .memsize (memsize))
   servant
     (.wb_clk (wb_clk),
      .wb_rst (wb_rst),
      .q (q));

endmodule

serv/servant/servant_clock_gen.v

`default_nettype none
module servant_clock_gen
  (
   input wire i_clk,
   output wire o_clk,
   output wire o_rst);

   parameter [79:0] PLL = "NONE";

   generate
      if ((PLL == "ICE40_CORE") || (PLL == "ICE40_PAD")) begin
ice40_pll #(.PLL (PLL)) pll
  (.i_clk (i_clk),
   .o_clk (o_clk),
   .o_rst (o_rst));
      end else begin
assign o_clk = i_clk;

reg [4:0] rst_reg = 5'b11111;

always @(posedge o_clk)
  rst_reg <= {1'b0, rst_reg[4:1]};
assign o_rst = rst_reg[0];
      end
   endgenerate
endmodule

build/servant_1.1.0/src/servant-catzip_pll_1.1.0/pll.vh

/**
 * PLL configuration
 *
 * This Verilog header file was generated automatically
 * using the icepll tool from the IceStorm project.
 * It is intended for use with FPGA primitives SB_PLL40_CORE,
 * SB_PLL40_PAD, SB_PLL40_2_PAD, SB_PLL40_2F_CORE or SB_PLL40_2F_PAD.
 * Use at your own risk.
 *
 * Given input frequency: 100.000 MHz
 * Requested output frequency: 40.000 MHz
 * Achieved output frequency: 40.000 MHz
 */

.FEEDBACK_PATH("SIMPLE"),
.DIVR(4'b0100),	// DIVR = 4
.DIVF(7'b0011111),	// DIVF = 31
.DIVQ(3'b100),	// DIVQ = 4
.FILTER_RANGE(3'b010)	// FILTER_RANGE = 2

serv/servant/servant.v
serv/servant/servant_abriter.v
serv/servant/servant_mux.v
serv/servant/servant_ram.v
serv/servant/servant_gpio.v
`default_nettype none
module servant
(
 input wire wb_clk,
 input wire wb_rst,
 output wire q);

   parameter memfile = "zephyr_hello.hex";
   parameter memsize = 8192;
   parameter reset_strategy = "MINI";
   parameter sim = 0;
   parameter with_csr = 1;

   wire	timer_irq;

   wire [31:0]	wb_ibus_adr;
   wire	wb_ibus_cyc;
   wire [31:0]	wb_ibus_rdt;
   wire	wb_ibus_ack;

   wire [31:0]	wb_dbus_adr;
   wire [31:0]	wb_dbus_dat;
   wire [3:0]	wb_dbus_sel;
   wire	wb_dbus_we;
   wire	wb_dbus_cyc;
   wire [31:0]	wb_dbus_rdt;
   wire	wb_dbus_ack;

   wire [31:0]	wb_dmem_adr;
   wire [31:0]	wb_dmem_dat;
   wire [3:0]	wb_dmem_sel;
   wire	wb_dmem_we;
   wire	wb_dmem_cyc;
   wire [31:0]	wb_dmem_rdt;
   wire	wb_dmem_ack;

   wire [31:0]	wb_mem_adr;
   wire [31:0]	wb_mem_dat;
   wire [3:0]	wb_mem_sel;
   wire	wb_mem_we;
   wire	wb_mem_cyc;
   wire [31:0]	wb_mem_rdt;
   wire	wb_mem_ack;

   wire	wb_gpio_dat;
   wire	wb_gpio_we;
   wire	wb_gpio_cyc;
   wire	wb_gpio_rdt;

   wire [31:0]	wb_timer_dat;
   wire	wb_timer_we;
   wire	wb_timer_cyc;
   wire [31:0]	wb_timer_rdt;

   wire [31:0] mdu_rs1;
   wire [31:0] mdu_rs2;
   wire [ 2:0] mdu_op;
   wire mdu_valid;
   wire [31:0] mdu_rd;
   wire mdu_ready;

   servant_arbiter arbiter
     (.i_wb_cpu_dbus_adr (wb_dmem_adr),
      .i_wb_cpu_dbus_dat (wb_dmem_dat),
      .i_wb_cpu_dbus_sel (wb_dmem_sel),
      .i_wb_cpu_dbus_we (wb_dmem_we ),
      .i_wb_cpu_dbus_cyc (wb_dmem_cyc),
      .o_wb_cpu_dbus_rdt (wb_dmem_rdt),
      .o_wb_cpu_dbus_ack (wb_dmem_ack),

      .i_wb_cpu_ibus_adr (wb_ibus_adr),
      .i_wb_cpu_ibus_cyc (wb_ibus_cyc),
      .o_wb_cpu_ibus_rdt (wb_ibus_rdt),
      .o_wb_cpu_ibus_ack (wb_ibus_ack),

      .o_wb_cpu_adr (wb_mem_adr),
      .o_wb_cpu_dat (wb_mem_dat),
      .o_wb_cpu_sel (wb_mem_sel),
      .o_wb_cpu_we (wb_mem_we ),
      .o_wb_cpu_cyc (wb_mem_cyc),
      .i_wb_cpu_rdt (wb_mem_rdt),
      .i_wb_cpu_ack (wb_mem_ack));

   servant_mux #(sim) servant_mux
     (
      .i_clk (wb_clk),
      .i_rst (wb_rst & (reset_strategy != "NONE")),
      .i_wb_cpu_adr (wb_dbus_adr),
      .i_wb_cpu_dat (wb_dbus_dat),
      .i_wb_cpu_sel (wb_dbus_sel),
      .i_wb_cpu_we (wb_dbus_we),
      .i_wb_cpu_cyc (wb_dbus_cyc),
      .o_wb_cpu_rdt (wb_dbus_rdt),
      .o_wb_cpu_ack (wb_dbus_ack),

      .o_wb_mem_adr (wb_dmem_adr),
      .o_wb_mem_dat (wb_dmem_dat),
      .o_wb_mem_sel (wb_dmem_sel),
      .o_wb_mem_we (wb_dmem_we),
      .o_wb_mem_cyc (wb_dmem_cyc),
      .i_wb_mem_rdt (wb_dmem_rdt),

      .o_wb_gpio_dat (wb_gpio_dat),
      .o_wb_gpio_we (wb_gpio_we),
      .o_wb_gpio_cyc (wb_gpio_cyc),
      .i_wb_gpio_rdt (wb_gpio_rdt),

      .o_wb_timer_dat (wb_timer_dat),
      .o_wb_timer_we (wb_timer_we),
      .o_wb_timer_cyc (wb_timer_cyc),
      .i_wb_timer_rdt (wb_timer_rdt));

   servant_ram
     #(.memfile (memfile),
       .depth (memsize),
       .RESET_STRATEGY (reset_strategy))
   ram
     (// Wishbone interface
      .i_wb_clk (wb_clk),
      .i_wb_rst (wb_rst),
      .i_wb_adr (wb_mem_adr[$clog2(memsize)-1:2]),
      .i_wb_cyc (wb_mem_cyc),
      .i_wb_we (wb_mem_we) ,
      .i_wb_sel (wb_mem_sel),
      .i_wb_dat (wb_mem_dat),
      .o_wb_rdt (wb_mem_rdt),
      .o_wb_ack (wb_mem_ack));

   generate
      if (with_csr) begin
servant_timer
  #(.RESET_STRATEGY (reset_strategy),
    .WIDTH (32))
timer
  (.i_clk (wb_clk),
   .i_rst (wb_rst),
   .o_irq (timer_irq),
   .i_wb_cyc (wb_timer_cyc),
   .i_wb_we (wb_timer_we) ,
   .i_wb_dat (wb_timer_dat),
   .o_wb_dat (wb_timer_rdt));
      end else begin
assign wb_timer_rdt = 32'd0;
assign timer_irq = 1'b0;
      end
   endgenerate

   servant_gpio gpio
     (.i_wb_clk (wb_clk),
      .i_wb_dat (wb_gpio_dat),
      .i_wb_we (wb_gpio_we),
      .i_wb_cyc (wb_gpio_cyc),
      .o_wb_rdt (wb_gpio_rdt),
      .o_gpio (q));

   serv_rf_top
     #(.RESET_PC (32'h0000_0000),
       .RESET_STRATEGY (reset_strategy),
  `ifdef MDU
       .MDU(1),
  `endif
       .WITH_CSR (with_csr))
   cpu
     (
      .clk (wb_clk),
      .i_rst (wb_rst),
      .i_timer_irq (timer_irq),
`ifdef RISCV_FORMAL
      .rvfi_valid (),
      .rvfi_order (),
      .rvfi_insn (),
      .rvfi_trap (),
      .rvfi_halt (),
      .rvfi_intr (),
      .rvfi_mode (),
      .rvfi_ixl (),
      .rvfi_rs1_addr (),
      .rvfi_rs2_addr (),
      .rvfi_rs1_rdata (),
      .rvfi_rs2_rdata (),
      .rvfi_rd_addr (),
      .rvfi_rd_wdata (),
      .rvfi_pc_rdata (),
      .rvfi_pc_wdata (),
      .rvfi_mem_addr (),
      .rvfi_mem_rmask (),
      .rvfi_mem_wmask (),
      .rvfi_mem_rdata (),
      .rvfi_mem_wdata (),
`endif

      .o_ibus_adr (wb_ibus_adr),
      .o_ibus_cyc (wb_ibus_cyc),
      .i_ibus_rdt (wb_ibus_rdt),
      .i_ibus_ack (wb_ibus_ack),

      .o_dbus_adr (wb_dbus_adr),
      .o_dbus_dat (wb_dbus_dat),
      .o_dbus_sel (wb_dbus_sel),
      .o_dbus_we (wb_dbus_we),
      .o_dbus_cyc (wb_dbus_cyc),
      .i_dbus_rdt (wb_dbus_rdt),
      .i_dbus_ack (wb_dbus_ack),

      //Extension
      .o_ext_rs1 (mdu_rs1),
      .o_ext_rs2 (mdu_rs2),
      .o_ext_funct3 (mdu_op),
      .i_ext_rd (mdu_rd),
      .i_ext_ready (mdu_ready),
      //MDU
      .o_mdu_valid (mdu_valid));

`ifdef MDU
    mdu_top mdu_serv
    (
     .i_clk(wb_clk),
     .i_rst(wb_rst),
     .i_mdu_rs1(mdu_rs1),
     .i_mdu_rs2(mdu_rs2),
     .i_mdu_op(mdu_op),
     .i_mdu_valid(mdu_valid),
     .o_mdu_ready(mdu_ready),
     .o_mdu_rd(mdu_rd));
`else
    assign mdu_ready = 1'b0;
    assign mdu_rd = 32'b0;
`endif

endmodule

serv/servant/servant_arbiter.v

/* Arbitrates between dbus and ibus accesses.
 * Relies on the fact that not both masters are active at the same time
 */
module servant_arbiter
  (
   input wire [31:0] i_wb_cpu_dbus_adr,
   input wire [31:0] i_wb_cpu_dbus_dat,
   input wire [3:0] i_wb_cpu_dbus_sel,
   input wire	i_wb_cpu_dbus_we,
   input wire	i_wb_cpu_dbus_cyc,
   output wire [31:0] o_wb_cpu_dbus_rdt,
   output wire	o_wb_cpu_dbus_ack,

   input wire [31:0] i_wb_cpu_ibus_adr,
   input wire	i_wb_cpu_ibus_cyc,
   output wire [31:0] o_wb_cpu_ibus_rdt,
   output wire	o_wb_cpu_ibus_ack,

   output wire [31:0] o_wb_cpu_adr,
   output wire [31:0] o_wb_cpu_dat,
   output wire [3:0] o_wb_cpu_sel,
   output wire	o_wb_cpu_we,
   output wire	o_wb_cpu_cyc,
   input wire [31:0] i_wb_cpu_rdt,
   input wire	i_wb_cpu_ack);

   assign o_wb_cpu_dbus_rdt = i_wb_cpu_rdt;
   assign o_wb_cpu_dbus_ack = i_wb_cpu_ack & !i_wb_cpu_ibus_cyc;

   assign o_wb_cpu_ibus_rdt = i_wb_cpu_rdt;
   assign o_wb_cpu_ibus_ack = i_wb_cpu_ack & i_wb_cpu_ibus_cyc;

   assign o_wb_cpu_adr = i_wb_cpu_ibus_cyc ? i_wb_cpu_ibus_adr : i_wb_cpu_dbus_adr;
   assign o_wb_cpu_dat = i_wb_cpu_dbus_dat;
   assign o_wb_cpu_sel = i_wb_cpu_dbus_sel;
   assign o_wb_cpu_we = i_wb_cpu_dbus_we & !i_wb_cpu_ibus_cyc;
   assign o_wb_cpu_cyc = i_wb_cpu_ibus_cyc | i_wb_cpu_dbus_cyc;

endmodule

serv/servant/servant_mux.v

/* Arbitrates between dbus and ibus accesses.
 * Relies on the fact that not both masters are active at the same time
 */
module servant_arbiter
  (
   input wire [31:0] i_wb_cpu_dbus_adr,
   input wire [31:0] i_wb_cpu_dbus_dat,
   input wire [3:0] i_wb_cpu_dbus_sel,
   input wire	i_wb_cpu_dbus_we,
   input wire	i_wb_cpu_dbus_cyc,
   output wire [31:0] o_wb_cpu_dbus_rdt,
   output wire	o_wb_cpu_dbus_ack,

   input wire [31:0] i_wb_cpu_ibus_adr,
   input wire	i_wb_cpu_ibus_cyc,
   output wire [31:0] o_wb_cpu_ibus_rdt,
   output wire	o_wb_cpu_ibus_ack,

   output wire [31:0] o_wb_cpu_adr,
   output wire [31:0] o_wb_cpu_dat,
   output wire [3:0] o_wb_cpu_sel,
   output wire	o_wb_cpu_we,
   output wire	o_wb_cpu_cyc,
   input wire [31:0] i_wb_cpu_rdt,
   input wire	i_wb_cpu_ack);

   assign o_wb_cpu_dbus_rdt = i_wb_cpu_rdt;
   assign o_wb_cpu_dbus_ack = i_wb_cpu_ack & !i_wb_cpu_ibus_cyc;

   assign o_wb_cpu_ibus_rdt = i_wb_cpu_rdt;
   assign o_wb_cpu_ibus_ack = i_wb_cpu_ack & i_wb_cpu_ibus_cyc;

   assign o_wb_cpu_adr = i_wb_cpu_ibus_cyc ? i_wb_cpu_ibus_adr : i_wb_cpu_dbus_adr;
   assign o_wb_cpu_dat = i_wb_cpu_dbus_dat;
   assign o_wb_cpu_sel = i_wb_cpu_dbus_sel;
   assign o_wb_cpu_we = i_wb_cpu_dbus_we & !i_wb_cpu_ibus_cyc;
   assign o_wb_cpu_cyc = i_wb_cpu_ibus_cyc | i_wb_cpu_dbus_cyc;

endmodule

serv/servant/servant_ram.v

/* Arbitrates between dbus and ibus accesses.
 * Relies on the fact that not both masters are active at the same time
 */
module servant_arbiter
  (
   input wire [31:0] i_wb_cpu_dbus_adr,
   input wire [31:0] i_wb_cpu_dbus_dat,
   input wire [3:0] i_wb_cpu_dbus_sel,
   input wire	i_wb_cpu_dbus_we,
   input wire	i_wb_cpu_dbus_cyc,
   output wire [31:0] o_wb_cpu_dbus_rdt,
   output wire	o_wb_cpu_dbus_ack,

   input wire [31:0] i_wb_cpu_ibus_adr,
   input wire	i_wb_cpu_ibus_cyc,
   output wire [31:0] o_wb_cpu_ibus_rdt,
   output wire	o_wb_cpu_ibus_ack,

   output wire [31:0] o_wb_cpu_adr,
   output wire [31:0] o_wb_cpu_dat,
   output wire [3:0] o_wb_cpu_sel,
   output wire	o_wb_cpu_we,
   output wire	o_wb_cpu_cyc,
   input wire [31:0] i_wb_cpu_rdt,
   input wire	i_wb_cpu_ack);

   assign o_wb_cpu_dbus_rdt = i_wb_cpu_rdt;
   assign o_wb_cpu_dbus_ack = i_wb_cpu_ack & !i_wb_cpu_ibus_cyc;

   assign o_wb_cpu_ibus_rdt = i_wb_cpu_rdt;
   assign o_wb_cpu_ibus_ack = i_wb_cpu_ack & i_wb_cpu_ibus_cyc;

   assign o_wb_cpu_adr = i_wb_cpu_ibus_cyc ? i_wb_cpu_ibus_adr : i_wb_cpu_dbus_adr;
   assign o_wb_cpu_dat = i_wb_cpu_dbus_dat;
   assign o_wb_cpu_sel = i_wb_cpu_dbus_sel;
   assign o_wb_cpu_we = i_wb_cpu_dbus_we & !i_wb_cpu_ibus_cyc;
   assign o_wb_cpu_cyc = i_wb_cpu_ibus_cyc | i_wb_cpu_dbus_cyc;

endmodule

serv/servant/servant_gpio.v

module servant_gpio
  (input wire i_wb_clk,
   input wire i_wb_dat,
   input wire i_wb_we,
   input wire i_wb_cyc,
   output reg o_wb_rdt,
   output reg o_gpio);

   always @(posedge i_wb_clk) begin
      o_wb_rdt <= o_gpio;
      if (i_wb_cyc & i_wb_we)
o_gpio <= i_wb_dat;
   end
endmodule